#

# $Id: ser.cfg,v 1.21.4.1 2003/11/10 15:35:15 andrei Exp $

#

# simple quick-start config script

#

# ----------- global configuration parameters ------------------------

#debug=3         # debug level (cmd line: -dddddddddd)

#fork=yes

#log_stderror=no        # (cmd line: -E)

# Uncomment these lines to enter debugging mode

#debug=7

#fork=no

#log_stderror=yes

check_via=no    # (cmd. line: -v)

dns=no           # (cmd. line: -r)

rev_dns=no      # (cmd. line: -R)

#port=5060

#children=4

fifo="/tmp/ser_fifo"

alias="84.203.148.146:5060"

# ------------------ module loading ----------------------------------

# Uncomment this if you want to use SQL database

loadmodule "/usr/lib/ser/modules/mysql.so"

loadmodule "/usr/lib/ser/modules/sl.so"

loadmodule "/usr/lib/ser/modules/tm.so"

loadmodule "/usr/lib/ser/modules/rr.so"

loadmodule "/usr/lib/ser/modules/maxfwd.so"

loadmodule "/usr/lib/ser/modules/usrloc.so"

loadmodule "/usr/lib/ser/modules/registrar.so"

loadmodule "/usr/lib/ser/modules/textops.so"

loadmodule "/usr/lib/ser/modules/nathelper.so"

#loadmodule "/usr/lib/ser/modules/pa.so"

# Uncomment this if you want digest authentication

# mysql.so must be loaded !

loadmodule "/usr/lib/ser/modules/auth.so"

loadmodule "/usr/lib/ser/modules/auth_db.so"

# ----------------- setting module-specific parameters ---------------

# -- usrloc params --

#modparam("usrloc", "db_mode",   0)

# Uncomment this if you want to use SQL database

# for persistent storage and comment the previous line

modparam("usrloc", "db_mode", 2)

# -- auth params --

# Uncomment if you are using auth module

#

modparam("auth_db", "calculate_ha1", yes)

#

# If you set "calculate_ha1" parameter to yes (which true in this config),

# uncomment also the following parameter)

#

modparam("auth_db", "password_column", "password")

# -- rr params --

# add value to ;lr param to make some broken UAs happy

modparam("rr", "enable_full_lr", 11)

#!! Nathelper

modparam("registrar", "nat_flag", 60)

modparam("nathelper", "natping_interval", 10) #Ping interval 10 s

modparam("nathelper", "ping_nated_only", 1)   #Ping only clients behind NAT

modparam("nathelper", "rtpproxy_sock", "/var/run/rtpproxy.sock")

modparam("tm", "fr_inv_timer", 20)

# -------------------------  request routing logic -------------------

# main routing logic

route{

# initial sanity checks -- messages with

# max_forwards==0, or excessively long requests

if (!mf_process_maxfwd_header("10")) {

sl_send_reply("483","Too Many Hops");

break;

};

if ( msg:len > max_len ) {

sl_send_reply("513", "Message too big");

break;

};

if (nat_uac_test("3")){

if (method == "REGISTER" || ! search("^Record-Route:")){

log("Log: Someone trying to register from private IP,rew

riting\n");

fix_nated_contact(); #Rewrite contact with source IP

if (method == "INVITE"){

fix_nated_sdp("1"); #Add direction=active to SDP

};

force_rport(); # Add rport parameter to topmost Via

setflag(6); # Mark as Nated

};

};

###################################################################

# we record-route all messages -- to make sure that

# subsequent messages will go through our proxy; that's

# particularly good if upstream and downstream entities

# use different transport protocol

if (method =="REGISTER") record_route();

# loose-route processing

if (loose_route()) {

#commented 11/02/05

#t_relay();

route(1);

break;

};

# if the request is for other domain use UsrLoc

# (in case, it does not work, use the following command

# with proper names and addresses in it)

if (uri==myself) {

log(1,"into loop");

if (method=="REGISTER") {

# Uncomment this if you want to use digest authentication

#                       if (!www_authorize("84.203.148.146", "subscriber")) {

#                               www_challenge("84.203.148.146", "0");

#                               break;

#                       };

save("location");

break;

};

lookup("aliases");

if (!uri==myself) {

append_hf("P-hint: outbound alias\r\n");

route(1);

break;

};

if (method=="INVITE"){

log(1,"in invite loop");

#break; #no 100 trying

t_on_failure("1");

};

# native SIP destinations are handled using our USRLOC DB

if (!lookup("location")) {

#sl_send_reply("404", "Not Found");

route(2);

break;

};

};

# forward to current uri now; use stateful forwarding; that

# works reliably even if we forward from TCP to UDP

#commented 11/02/05#######################

if (!t_relay()) {

sl_reply_error();

};

#route(1);

}

##################################

route[1]

{

#!!Nathelper

if(uri=~"[@:](192\.168\.|10\.|172\.(1[6-9]|2[0-9]|3[0-1])\.)" && !search

("^Route:")){

sl_send_reply("479", "We don't forward to private IP addresses")

;

break;

};

if (isflagset(6)){

force_rtp_proxy();

}

t_on_reply("1");

if(!t_relay()){

sl_reply_error();

break;

};

}

######################################

#!! Nathelper

onreply_route[1] {

if(isflagset(6) && status =~ "(183)|2[0-9][0-9]"){

fix_nated_contact();

force_rtp_proxy();

}else if (nat_uac_test("1")){

fix_nated_contact();

};

}

########

# ------------- handling of unavailable user ------------------

route[2] {

# non-Voip -- just send "off-line"

if (!(method == "INVITE" || method == "ACK" || method == "CANCEL")) {

sl_send_reply("404", "Not Found");

break;

};

# forward to voicemail now

rewritehostport("84.203.148.146:5062");

t_relay_to_udp("84.203.148.146", "5062");

}

# if forwarding downstream did not succeed, try voicemail running

# at 84.203.148.146:5062

failure_route[1] {

revert_uri();

rewritehostport("84.203.148.146:5062");

append_branch();

t_relay_to_udp("84.203.148.146", "5062");

}

SER messages (ngrep SIP –q)

U 84.203.148.146:5060 -> 84.203.148.14:5062

INVITE sip:2093@84.203.148.14:5062 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146

;branch=z9hG4bK680b.f4a8b4c7.0..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4

bK2913fcd155954e44..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f

10f3..To: <sip:2093@84.203.148.146>..Contact: <sip:2092@84.203.148.14>..Sup

ported: replaces..Call-ID: 50f069f768526c91@172.16.3.30..CSeq: 6056 INVITE.

.User-Agent: Grandstream BT100 1.0.5.18..Max-Forwards: 69..Allow: INVITE,AC

K,CANCEL,BYE,NOTIFY,REFER,OPTIONS,INFO,SUBSCRIBE..Content-Type: application

/sdp..Content-Length: 424....v=0..o=2092 8000 0 IN IP4 84.203.148.14..s=SIP

Call..c=IN IP4 84.203.148.14..t=0 0..m=audio 5004 RTP/AVP 0 8 4 18 2 15 99

9 101..a=sendrecv..a=rtpmap:0 PCMU/8000/3..a=rtpmap:8 PCMA/8000/3..a=rtpma

p:4 G723/8000/3..a=rtpmap:18 G729/8000/3..a=rtpmap:2 G726-32/8000/3..a=rtpm

ap:15 G728/8000/3..a=rtpmap:99 iLBC/8000/3..a=fmtp:99 mode=20..a=rtpmap:9 G

722/8000/3..a=ptime:20..a=rtpmap:101 telephone-event/8000/3..a=fmtp:101 0-1

1..

U 84.203.148.146:5060 -> 84.203.148.14:5060

INVITE sip:2093@84.203.148.14 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146;bran

ch=z9hG4bK680b.f4a8b4c7.1..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK291

3fcd155954e44..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3.

.To: <sip:2093@84.203.148.146>..Contact: <sip:2092@84.203.148.14>..Supporte

d: replaces..Call-ID: 50f069f768526c91@172.16.3.30..CSeq: 6056 INVITE..User

-Agent: Grandstream BT100 1.0.5.18..Max-Forwards: 69..Allow: INVITE,ACK,CAN

CEL,BYE,NOTIFY,REFER,OPTIONS,INFO,SUBSCRIBE..Content-Type: application/sdp.

.Content-Length: 424....v=0..o=2092 8000 0 IN IP4 84.203.148.14..s=SIP Call

..c=IN IP4 84.203.148.14..t=0 0..m=audio 5004 RTP/AVP 0 8 4 18 2 15 99 9 10

1..a=sendrecv..a=rtpmap:0 PCMU/8000/3..a=rtpmap:8 PCMA/8000/3..a=rtpmap:4 G

723/8000/3..a=rtpmap:18 G729/8000/3..a=rtpmap:2 G726-32/8000/3..a=rtpmap:15

G728/8000/3..a=rtpmap:99 iLBC/8000/3..a=fmtp:99 mode=20..a=rtpmap:9 G722/8

000/3..a=ptime:20..a=rtpmap:101 telephone-event/8000/3..a=fmtp:101 0-11..

U 84.203.148.146:5060 -> 84.203.148.14:5061

INVITE sip:2093@84.203.148.14:5061 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146

;branch=z9hG4bK680b.f4a8b4c7.2..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4

bK2913fcd155954e44..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f

10f3..To: <sip:2093@84.203.148.146>..Contact: <sip:2092@84.203.148.14>..Sup

ported: replaces..Call-ID: 50f069f768526c91@172.16.3.30..CSeq: 6056 INVITE.

.User-Agent: Grandstream BT100 1.0.5.18..Max-Forwards: 69..Allow: INVITE,AC

K,CANCEL,BYE,NOTIFY,REFER,OPTIONS,INFO,SUBSCRIBE..Content-Type: application

/sdp..Content-Length: 424....v=0..o=2092 8000 0 IN IP4 84.203.148.14..s=SIP

Call..c=IN IP4 84.203.148.14..t=0 0..m=audio 5004 RTP/AVP 0 8 4 18 2 15 99

9 101..a=sendrecv..a=rtpmap:0 PCMU/8000/3..a=rtpmap:8 PCMA/8000/3..a=rtpma

p:4 G723/8000/3..a=rtpmap:18 G729/8000/3..a=rtpmap:2 G726-32/8000/3..a=rtpm

ap:15 G728/8000/3..a=rtpmap:99 iLBC/8000/3..a=fmtp:99 mode=20..a=rtpmap:9 G

722/8000/3..a=ptime:20..a=rtpmap:101 telephone-event/8000/3..a=fmtp:101 0-1

1..

U 84.203.148.14:5060 -> 84.203.148.146:5060

SIP/2.0 100 Trying..Via: SIP/2.0/UDP 84.203.148.146;branch=z9hG4bK680b.f4a8

b4c7.1..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd155954e44..From

: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <sip:2093@84.2

03.148.146>..Call-ID: 50f069f768526c91@172.16.3.30..CSeq: 6056 INVITE..User

-Agent: Grandstream BT100 1.0.5.18..Content-Length: 0....

U 84.203.148.14:5060 -> 84.203.148.146:5060

SIP/2.0 486 Busy..Via: SIP/2.0/UDP 84.203.148.146;branch=z9hG4bK680b.f4a8b4

c7.1..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd155954e44..From:

"2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <sip:2093@84.203

.148.146>;tag=feda04a1233f11d4..Call-ID: 50f069f768526c91@172.16.3.30..CSeq

: 6056 INVITE..User-Agent: Grandstream BT100 1.0.5.18..Content-Length: 0...

.

U 84.203.148.146:5060 -> 84.203.148.14:5060

ACK sip:2093@84.203.148.14 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146;branch=

z9hG4bK680b.f4a8b4c7.1..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0

222f10f3..Call-ID: 50f069f768526c91@172.16.3.30..To: <sip:2093@84.203.148.1

46>;tag=feda04a1233f11d4..CSeq: 6056 ACK..User-Agent: Sip EXpress router(0.

8.14 (i386/linux))..Content-Length: 0....

U 84.203.148.14:5061 -> 84.203.148.146:5060

SIP/2.0 100 Trying..Via: SIP/2.0/UDP 84.203.148.146;branch=z9hG4bK680b.f4a8

b4c7.2..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd155954e44..From

: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <sip:2093@84.2

03.148.146>..Call-ID: 50f069f768526c91@172.16.3.30..CSeq: 6056 INVITE..User

-Agent: Grandstream BT100 1.0.5.18..Content-Length: 0....

U 84.203.148.14:5061 -> 84.203.148.146:5060

SIP/2.0 180 Ringing..Via: SIP/2.0/UDP 84.203.148.146;branch=z9hG4bK680b.f4a

8b4c7.2..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd155954e44..Fro

m: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <sip:2093@84.

203.148.146>;tag=9c06e8fcd5384c1f..Call-ID: 50f069f768526c91@172.16.3.30..C

Seq: 6056 INVITE..User-Agent: Grandstream BT100 1.0.5.18..Content-Length: 0

....

U 84.203.148.146:5060 -> 84.203.148.14:5060

SIP/2.0 180 Ringing..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd15

5954e44..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <

sip:2093@84.203.148.146>;tag=9c06e8fcd5384c1f..Call-ID: 50f069f768526c91@17

2.16.3.30..CSeq: 6056 INVITE..User-Agent: Grandstream BT100 1.0.5.18..Conte

nt-Length: 0....

U 84.203.148.146:5060 -> 84.203.148.14:5062

INVITE sip:2093@84.203.148.14:5062 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146

;branch=z9hG4bK680b.f4a8b4c7.0..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4

bK2913fcd155954e44..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f

10f3..To: <sip:2093@84.203.148.146>..Contact: <sip:2092@84.203.148.14>..Sup

ported: replaces..Call-ID: 50f069f768526c91@172.16.3.30..CSeq: 6056 INVITE.

.User-Agent: Grandstream BT100 1.0.5.18..Max-Forwards: 69..Allow: INVITE,AC

K,CANCEL,BYE,NOTIFY,REFER,OPTIONS,INFO,SUBSCRIBE..Content-Type: application

/sdp..Content-Length: 424....v=0..o=2092 8000 0 IN IP4 84.203.148.14..s=SIP

Call..c=IN IP4 84.203.148.14..t=0 0..m=audio 5004 RTP/AVP 0 8 4 18 2 15 99

9 101..a=sendrecv..a=rtpmap:0 PCMU/8000/3..a=rtpmap:8 PCMA/8000/3..a=rtpma

p:4 G723/8000/3..a=rtpmap:18 G729/8000/3..a=rtpmap:2 G726-32/8000/3..a=rtpm

ap:15 G728/8000/3..a=rtpmap:99 iLBC/8000/3..a=fmtp:99 mode=20..a=rtpmap:9 G

722/8000/3..a=ptime:20..a=rtpmap:101 telephone-event/8000/3..a=fmtp:101 0-1

1..

U 84.203.148.14:5061 -> 84.203.148.146:5060

SIP/2.0 200 OK..Via: SIP/2.0/UDP 84.203.148.146;branch=z9hG4bK680b.f4a8b4c7

.2..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd155954e44..From: "2

092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <sip:2093@84.203.1

48.146>;tag=9c06e8fcd5384c1f..Call-ID: 50f069f768526c91@172.16.3.30..CSeq:

6056 INVITE..User-Agent: Grandstream BT100 1.0.5.18..Contact: <sip:2093@84.

203.148.14:5061>..Allow: INVITE,ACK,CANCEL,BYE,NOTIFY,REFER,OPTIONS,INFO,SU

BSCRIBE..Content-Type: application/sdp..Supported: replaces..Content-Length

: 156....v=0..o=2093 8000 0 IN IP4 84.203.148.14..s=SIP Call..c=IN IP4 84.2

03.148.14..t=0 0..m=audio 5005 RTP/AVP 0..a=sendrecv..a=rtpmap:0 PCMU/8000/

3..a=ptime:20..

U 84.203.148.146:5060 -> 84.203.148.14:5060

SIP/2.0 200 OK..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4bK2913fcd155954e

44..From: "2092" <sip:2092@84.203.148.146>;tag=bec86fa0222f10f3..To: <sip:2

093@84.203.148.146>;tag=9c06e8fcd5384c1f..Call-ID: 50f069f768526c91@172.16.

3.30..CSeq: 6056 INVITE..User-Agent: Grandstream BT100 1.0.5.18..Contact: <

sip:2093@84.203.148.14:5061>..Allow: INVITE,ACK,CANCEL,BYE,NOTIFY,REFER,OPT

IONS,INFO,SUBSCRIBE..Content-Type: application/sdp..Supported: replaces..Co

ntent-Length: 156....v=0..o=2093 8000 0 IN IP4 84.203.148.14..s=SIP Call..c

=IN IP4 84.203.148.14..t=0 0..m=audio 5005 RTP/AVP 0..a=sendrecv..a=rtpmap:

0 PCMU/8000/3..a=ptime:20..

.148.14;branch=z9hG4bK183398ddcafd8498..From: "2092" <sip:2092@84.203.148.1

46>;tag=be7cb43de905b4c3..To: <sip:2093@84.203.148.146>..Call-ID: f39efe91b

65eee43@172.16.3.30..CSeq: 54926 INVITE..Server: Sip EXpress router (0.8.14

(i386/linux))..Content-Length: 0..Warning: 392 84.203.148.146:5060 "Noisy

feedback tells:  pid=22638 req_src_ip=84.203.148.14 req_src_port=5060 in_ur

i=sip:2093@84.203.148.146 out_uri=sip:2093@84.203.148.14:5061 via_cnt==1"..

..

U 84.203.148.146:5060 -> 84.203.148.14:5061

INVITE sip:2093@84.203.148.14:5061 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146

;branch=z9hG4bK94e.9d6e2af6.0..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4b

K183398ddcafd8498..From: "2092" <sip:2092@84.203.148.146>;tag=be7cb43de905b

4c3..To: <sip:2093@84.203.148.146>..Contact: <sip:2092@84.203.148.14>..Supp

orted: replaces..Call-ID: f39efe91b65eee43@172.16.3.30..CSeq: 54926 INVITE.

.User-Agent: Grandstream BT100 1.0.5.18..Max-Forwards: 69..Allow: INVITE,AC

K,CANCEL,BYE,NOTIFY,REFER,OPTIONS,INFO,SUBSCRIBE..Content-Type: application

/sdp..Content-Length: 424....v=0..o=2092 8000 0 IN IP4 84.203.148.14..s=SIP

Call..c=IN IP4 84.203.148.14..t=0 0..m=audio 5004 RTP/AVP 0 8 4 18 2 15 99

9 101..a=sendrecv..a=rtpmap:0 PCMU/8000/3..a=rtpmap:8 PCMA/8000/3..a=rtpma

p:4 G723/8000/3..a=rtpmap:18 G729/8000/3..a=rtpmap:2 G726-32/8000/3..a=rtpm

ap:15 G728/8000/3..a=rtpmap:99 iLBC/8000/3..a=fmtp:99 mode=20..a=rtpmap:9 G

722/8000/3..a=ptime:20..a=rtpmap:101 telephone-event/8000/3..a=fmtp:101 0-1

1..

U 84.203.148.146:5060 -> 84.203.148.14:5061

INVITE sip:2093@84.203.148.14:5061 SIP/2.0..Via: SIP/2.0/UDP 84.203.148.146

;branch=z9hG4bK94e.9d6e2af6.0..Via: SIP/2.0/UDP 84.203.148.14;branch=z9hG4b

K183398ddcafd8498..From: "2092" <sip:2092@84.203.148.146>;tag=be7cb43de905b

4c3..To: <sip:2093@84.203.148.146>..Contact: <sip:2092@84.203.148.14>..Supp

orted: replaces..Call-ID: f39efe91b65eee43@172.16.3.30..CSeq: 54926 INVITE.

.User-Agent: Grandstream BT100 1.0.5.18..Max-Forwards: 69..Allow: